## Slide 1: Introduction to Autonomous System Numbers (ASN)
Gateway Operations

## Slide 2
What is an Autonomous System Number?
Autonomous System Numbers (ASNs) are globally unique identifiers for IP networks
ASNs are allocated to each Autonomous System (AS) for use in BGP routing
AS numbers are important because the ASN uniquely identifies each network on the Internet

## Slide 3
When Do I Need An ASN?
An ASN is needed if you have a Multi-homed network to different providers
Routing policy different to external peers
* For more information please refer to RFC1930: Guidelines for creation, selection and registration of an Autonomous System

## Slide 4
Representation Of Routing Policy
Routing and packet flows
announces
accepts
announces
accepts
Packet Flow
Traffic Flow
Packet Flow
AS 1
AS 2
For AS1 and AS2 networks to communicate
AS1 must announce to AS2
AS2 must accept from AS1
AS2 must announce to AS1
AS1 must accept from AS2

## Slide 5
AS Number Representation
2-byte only AS number range
0 – 65535
4-byte only AS number range
AS PLAIN: 65,536 - 4,294,967,295
AS DOT: 1.0 - 65535.65535
APNIC region uses the AS PLAIN style of numbering